## Slide 1: The MTU Manifesto
04-Feb-2025

## Slide 2: Preamble
04-Feb-2025

## Slide 3: Who is this person talking to you?
I’ve been “doing network stuff” for just over 25 years
Long-time network architect…
  …first-time NANOG-er
Notes: HELLO, NANOG 93!!!

## Slide 4: Context
For just over 25 years now, I’ve been plagued by “MTU issues”
What gives?
  Is there something fundamentally unsolvable?
  Is there something we’re all just doing wrong?
  Did this all get fixed, and I just missed a memo?
Notes: It’s a mad, mad, mad, mad (network) world
  Prevailing norms re. MTU in the enterprise network pre-date several features of contemporary enterprise networks
    Norms
      Enable “jumbo frames” and ~9K L3 MTU on all of your data-center switches
      Enable large-MTU on a per-host basis based on anticipated benefit at the application layer
    Contemporary design elements
      Hybrid/multi-cloud footprints
      Overlay networks nested n-layers deep
      SDN/VNF functions that wouldn’t know (let alone generate) a packet-too-big message if it bit them on the I/O bus
  This can directly result in PMTUD blackholes and other “invisible” packet-loss
Applications pay the price
  Nothing is ever instrumented as well as it “should” be
  Even detecting MTU-related packet loss can be a weeks-long odyssey
    Spent over a month once figuring out that an application was failing because the container image in a K8s pod “believed” it had a 1515-byte L2 MRU on its network interface
    And the same again realizing that the K8s orchestrator (who shall remain nameless) SDN controller had a logic-error in how it was populating flow-rules in the worker-node’s vswitch
  Nobody wants the overhead of state maintenance or guaranteed lossless performance
  Applications are “not UN-likely” to assume that “the network” will provide both
  The variety and prevalence of scenarios in which sub-optimal MTU configuration can result in the un-anticipated discarding of packets should give any enterprise network operators significant pause

## Slide 5: Agenda
Assumptions
(Please pardon my) Jargon
The List of Grievances
The Three Indictments
The List of Demands
Paths to MTU(topia)?
Q and A
Notes: In keeping with this talk’s title (“The MTU Manifesto”) I aimed for a structure somewhere between Martin Luther’s 95 theses and a grease-stained pamphlet attempting to debunk the moon landing.
We begin with a list of assumptions that informed my thinking as I approached the subject. As “assumptions” I won’t attempt to prove them today, but if you disagree with more than one of them, you’ll probably get more of a “grease-stained moon-landing debunking” vibe to the remainder of the talk
Then, I’ll define a few neologisms that I’ll be using throughout the remainder of the slides
Next, I will present the List of Grievances (I considered “accusations”, but that seemed overly combative.)
Following the grievances, I’ll proceed with detailed “indictments” of each of the grievances
At the heart of every good manifesto, lies the list of demands! Here I present the things that I propose MUST change.
Not wanting to end on such a rude and demanding note, I’ll close with an overview of a few hypothetical paths to what I call MTU-Topia!
And, of course, we’ll finish up with a few minutes for Q and A, because I completely forgot that the key to a really good manifesto is to publish it anonymously!

## Slide 6: Assumptions
04-Feb-2025

## Slide 7: Assumptions (1)
  Many applications recover gracefully from path MTU discovery (PMTUD) blackholes
  A non-trivial portion of applications don’t MTU dysfunction abounds in modern networks
Notes: Assumptions guiding this analysis
TCP itself can survive a PMTUD blackhole, albeit with an obnoxious sawtooth throughput pattern is it backs off from, eases back towards, and eventually exceeds to effective MTU and repeats the cycle

## Slide 8: Assumptions (2)
  There are valid use-cases for jumbo Ethernet
  PMTUD is preferable to manually decreasing interface MTU
  The cure should never be worse than the disease
Notes: Assumptions guiding this analysis
Compelling use-cases for jumbo Ethernet frames
  The “throw more MTU at the underlay” strategy we’ll discuss later
  Storage-over-IP protocols, which can get real performance improvements from being able to send an entire storage block in a single packet

## Slide 9: (Please Pardon) My Jargon
04-Feb-2025

## Slide 10: Path MTU Discovery
Path MTU discovery (PMTUD)
  Uses ICMP, relies on transit hops to participate
  Affects all IP traffic from host A to host B
Packetization Layer PMTUD (PLPMTUD)
  Uses packetization layer (TCP) to infer path MTU, only requires endpoints to participate
  Only affects the specific packetization-layer socket
Datagram PLPMTUD (DPLPMTUD)
  PLPMTUD, but for datagram protocols
  Has to be implemented at the application layer
Notes: More about these in the slides I won’t have time for.

## Slide 11: Stack Adjacency
The relationship between two interfaces directly above/below each other in the network stack
“Layer N” interface notated as: “If:L(n)”
Interface immediately above “If:L(n)” in the stack notated as: “If:L(n+1)”
If:L(n) is “downstack-adjacent” to If:L(n+1)
If:L(n+1) is “upstack-adjacent” to If:L(n)
Notes: I’m going to spend a lot of time today focused on vertical interfaces between layers of the network stack.

## Slide 12: Overlay/Underlay Tunnel Endpoints
A Tunnel Endpoint (TEP) encapsulates packets from the overlay network into packets on the underlay network for transport. (And vice-versa.)
TEP interfaces are logically “between” overlay and underlay interfaces
Whether that neighboring relationship is vertical or horizontal is… hard to pin down.
Notes: I’m also going to spend a lot of time on Tunnel, overlay, and tunnel interfaces.
I’ll be discussing them exclusively in regards to the in-network-tunneling use-case
  I won’t explicitly address the host-VPN-client use-case

## Slide 13: MTU, Generalized
Interface MTU: The largest message that a message-oriented protocol interface will attempt to transmit to its downstack-adjacent interface
Effective MTU: The largest message that can be successfully transmitted between two endpoints
Path MTU: The largest message that an interface will attempt to send to a specific destination
Protocol MTU: The largest message permitted by the semantics of the interface’s native protocol
Notes: I’m going to generalize the MTU concept from IP and apply it to message-oriented protocols in general
Since I’m already taking liberties, I’m also going to add a 3rd differentiated type of MTU

## Slide 14: Maximum Payload Unit (MPU)
The maximum size payload that a message-oriented protocol interface can transmit in a single message
Cannot be greater than interface-MTU minus protocol encapsulation overhead
Notes: “Maximum Payload Unit”
  The maximum size payload that a message-oriented protocol interface can receive from an up-stack protocol instance and successfully transmit in a single message
  Intuitively, the optimal configuration state is for a Layer-(n) interface’s MPU to be equivalent to the Layer-(n+1) interface’s MTU
Why give a name at all?
  Only the Layer-n interface knows exactly what its MPU is

## Slide 15: Maximum Receive Unit (MRU)
The maximum size message that a message-oriented protocol interface will accept from its downstack-adjacent interfaces
Should not be higher than the protocol-MTU
Not a prescriptive element of IP or Ethernet protocol standards (but maybe it should be?)
A descriptive property of any message-oriented protocol interface
Notes: MRU isn’t part of the IP or Ethernet standards, it’s an observed property of network interfaces
  It is an element of the point-to-point protocol (RFC1661)
The “maximum receive unit” (aka “MRU”) is the inverse of the “MTU.”
  Why? For no other reason than I said so…
  It refers to the maximum size message that can be received from a downstack-adjacent interface
  Many networking equipment vendors allow for explicit configuration of MRU values on Layer-2 interfaces
  While many operating-system network drivers will implement an implicit MRU that is equivalent to the explicitly configured MTU.
  Still others will have “invisible” MRUs that may be larger than the interface’s configured MTU, and can only be ascertained through trial and error.
  Not “…the message must be discarded”, in a prescriptive sense
    But “is discarded”, in a descriptive sense

## Slide 16: The List of Grievances
04-Feb-2025

## Slide 17: Vertical Interface Design in Message-Oriented Protocols
Does not expose the interface’s MPU to upstack-adjacent interfaces
Does not consume the downstack-adjacent interface’s MPU to infer its own MTU
This breaks the value of layered architectures, forcing us to go outside the stack to get L(n-1) information in order to configure L(n)
Notes: My first grievance is a foundational one

## Slide 18: IP overlays / “In-network-tunneling” Break PMTUD for the Overlay
It’s literally not possible for an IP-tunneling interface to infer enough from an underlay PTB message to translate it into the overlay network

## Slide 19: Common Design Practices Exacerbate MTU Issues
Stacked overlays
Encapsulating protocols with variable header lengths
Heterogenous L(n) MTUs in the same L(n) broadcast domain
Notes: It’s a mad, mad, mad, mad (network) world
  Prevailing norms re. MTU in the enterprise network pre-date several features of contemporary enterprise networks
    Norms
      Enable “jumbo frames” and ~9K L3 MTU on all of your data-center switches
      Enable large-MTU on a per-host basis based on anticipated benefit at the application layer
    Contemporary design elements
      Hybrid/multi-cloud footprints
      Overlay networks nested n-layers deep
      SDN/VNF functions that wouldn’t know (let alone generate) a packet-too-big message if it bit them on the I/O bus
  This can directly result in PMTUD blackholes and other “invisible” packet-loss
Applications pay the price
  Nothing is ever instrumented as well as it “should” be
  Even detecting MTU-related packet loss can be a weeks-long odyssey
    Spent over a month once figuring out that an application was failing because the container image in a K8s pod “believed” it had a 1515-byte L2 MRU on its network interface
    And the same again realizing that the K8s orchestrator (who shall remain nameless) SDN controller had a logic-error in how it was populating flow-rules in the worker-node’s vswitch
  Nobody wants the overhead of state maintenance or guaranteed lossless performance
  Applications are “not UN-likely” to assume that “the network” will provide both
  The variety and prevalence of scenarios in which sub-optimal MTU configuration can result in the un-anticipated discarding of packets should give any enterprise network operators significant pause

## Slide 20: Indictment of Vertical Interface Design (of message-oriented protocols)
04-Feb-2025

## Slide 21: Lack of Downstack MPU Visibility
Knowledge of If:L(n-1) MPU is required in order to infer the validity of an If:L(n) interface MTU value.
We don’t expose MPU to upstack-adjacent interfaces
As a result, If:L(n) MTU configuration requires inferences made at “Layer 8”, based on detailed knowledge of L(n-1)’s operation
Notes: This is not working out well for us
If the IP interface could see that its downstack-adjacent Ethernet interface had an MPU of 1500 bytes, it could safely infer an MTU of 1500 bytes.
  Or at least make that inference available to the switch operator

## Slide 22: Variable Encapsulation Overhead
This would be a non-issue if we had up-stack signaling of MPU, to enable auto-configuration of interface MTU.
Instead, network operators have a more complicated analysis for selecting an L(n) MTU if L(n) has variable encapsulation overhead:
Is If:L(n-1)’s MPU static or dynamic?
  If static, infer the actual If:L(n-1) MPU (by inferring encapsulation overhead from configuration
  If dynamic, infer the lowest possible If:L(n-1) MPU
Use inferred If:L(n-1) MPU as If:L(n) interface MTU
Notes: GENEVE is my favorite (OK, only) go-to example.
Bottom line, using protocols with variable encapsulation overhead makes the “Layer 8” call that much more labor intensive.

## Slide 23: MRU Opacity
This isn’t really a vertical-interface issue
It’s a Layer-8 issue, created by
We need to know If:L(n)’s MRU to inform our inferred optimal interface MTUs for:
  If:L(n)a-z
  If:L(n-1)a-z
  If:L(n+1)a-z
Notes: Example
  You have a VLAN on which
    Some workload needs a large-sized MTU (say, 8600-bytes)
    Other workload can’t/won’t allow you to configure anything above a 1500-byte MTU
    Is this SAFE?
      The only way to KNOW the answer to that, is to know the IP MRU of all those hosts with 1500-byte MTUs
        Do their NICs “support” jumbo frames? Will they pass an 8600-byte IP datagram upstack to the IP interface if one is received?
          If yes, will the IP interface accept that packet, or will it discard it?
        I’ve seen inconsistent behavior in the wild; you pretty-much have to manually test with crafted packets.

## Slide 24: Current Workarounds
Manage interface MTU at Layer-8
  Do the math, to the best of your ability and knowledge
  When all else fails, use trial-and-error to zero in on actual effective MTU and set that as interface MTU
Strive for consistent end-to-end L(n-1) MPU across your L(n) networks
  If it’s always the same value, you only have to do the math once

## Slide 25: TL/DR: Vertical Interface Design
The absence of in-stack signaling of MPU/MRU in vertical-interface design of message-oriented protocols makes things really hard.
It pushes deterministic calculations about optimal interface MTU into the hands and heads of operators who often don’t have the information they need to make those calculations
Notes: It’s a mad, mad, mad, mad (network) world
  Prevailing norms re. MTU in the enterprise network pre-date several features of contemporary enterprise networks
    Norms
      Enable “jumbo frames” and ~9K L3 MTU on all of your data-center switches
      Enable large-MTU on a per-host basis based on anticipated benefit at the application layer
    Contemporary design elements
      Hybrid/multi-cloud footprints
      Overlay networks nested n-layers deep
      SDN/VNF functions that wouldn’t know (let alone generate) a packet-too-big message if it bit them on the I/O bus
  This can directly result in PMTUD blackholes and other “invisible” packet-loss
Applications pay the price
  Nothing is ever instrumented as well as it “should” be
  Even detecting MTU-related packet loss can be a weeks-long odyssey
    Spent over a month once figuring out that an application was failing because the container image in a K8s pod “believed” it had a 1515-byte L2 MRU on its network interface
    And the same again realizing that the K8s orchestrator (who shall remain nameless) SDN controller had a logic-error in how it was populating flow-rules in the worker-node’s vswitch
  Nobody wants the overhead of state maintenance or guaranteed lossless performance
  Applications are “not UN-likely” to assume that “the network” will provide both
  The variety and prevalence of scenarios in which sub-optimal MTU configuration can result in the un-anticipated discarding of packets should give any enterprise network operators significant pause

## Slide 26: Indictment of In-Network Tunneling / IP overlays
04-Feb-2025

## Slide 27: In-network tunneling / IP-overlay Breaks PMTUD
There’s not a working mechanism for underlay PMTU information to make it into the overlay
The entire underlay becomes a PMTUD blackhole for the overlay
Notes: This struck me as a bold statement (at first.)
“Surely”, I thought to myself, “someone would have pointed this out to me when I was cutting my teeth in the field!”

## Slide 28: How Can This Be?
Hosts and routers have different PMTUD obligations
Routers only have to generate PTB messages
  Not implement path MTU
Hosts have to implement/maintain path MTU state
Devices doing IP-overlay encapsulation are forwarding datagrams (like a router) and generating datagrams (like a host)
  And (usually) fulfilling the PMTUD obligations of neither role
Notes: I scrapped a few slides on the various flavors of PMTU discovery (they’re in an appendix to this deck), but what I’m talking about here is the “original” Path MTU Discovery defined in RFC 1191.
So, in PMTUD…

## Slide 29: Overlay/Underlay/Tunnel Interfaces
What happens when Eth-b receives a PTB to Tu-a?
  Does it send the PTB to Tu-a?
  Does Tu-a xlate the PTB into the overlay?
  Does Tu-a implement path MTU?
Status quo, basically nothing
Overlay
h1
Underlay
Eth-a
Eth-b
Tu-a
9000B
1500B
1400B
p
  Tu-a isn’t maintaining its own path-MTU state
  Tu-a isn’t translating the PTB into the overlay
Notes: So, here’s an unfortunately squashed picture of a router doing in-network tunneling. It has an overlay interface (Eth-a), an underlay interface (Eth-b), and a tunnel interface (Tu-a). There’s also an overlay host (h1).
So, if “h1” sends a 1500-byte packet that is destined “somewhere else”
It is received on Eth-a, which then…
Has to route it to Tu-a if the Eth-a/Tu-a a

## Slide 30: Why nothing?
If Tu-a receives a PTB from the underlay
The PTB itself doesn’t contain enough information to successfully translate it into the overlay
Tu-a typically doesn’t implement path-MTU because (?)…
  Everybody wants to buy “wire-speed” overlay capabilities
    And that’s not feasible(?) to implement in-ASIC?
Notes: Tu-a looks like an interface from the management-plane, but it’s obviously much more than that.
  It’s doing IP-in-IP encapsulation using some tunneling protocol (VXLAN, let’s say.)
  It’s probably not being handled by the same branch in the packet processing pipeline as other routed-interface traffic
If it is an interface on a router though, router p’s only PMTUD responsibilities are to
  Have an interface MTU to Tu-a
  Don’t send packets out Tu-a that are > Tu-a’s MTU
  Generate PTBs if it receives a packet with the DF-bit set that is bigger than Tu-a’s MTU
  NOTHING about
    Translating any PTBs it receives from the underlay into the overlay
    Maintaining its own path MTU for Tu-a
So…

## Slide 31: Current Workarounds
Overlay providers can declare much smaller MTUs on the overlay network services than on the underlay services and avoid the problem altogether
Overlay consumers can just decrease their interface MTUs for the same result

## Slide 32: TL/DR: In-Network Tunneling
In-network tunneling turns the entire underlay into a PMTUD-blackhole for the overlay
The lack of a clear solution probably has a lot to do with ambiguity as to the role* of tunnel interfaces
Existing workarounds boil down to either
  “Throw bigger MTU at the underlay”, or
  “Claw back MTU from the overlay”
Notes: *Are they “just” interfaces on a router? Or do they constitute a host in their own right? (WRT PMTUD.)
Are they vertical, or horizontal neighbors in the network stack?

## Slide 33: Indictment of Operators’ Design Practices
04-Feb-2025

## Slide 34: Encapsulation Ad Absurdum
It’s not uncommon to see three or more recursive overlay encapsulations
E.g. K8s VXLAN overlay on a hypervisor-networking GENEVE overlay on a data-center VXLAN overlay
That’s triple the risk of getting your math wonky while calculating what the nominal IP interface MTU should be.
Notes: Now, there’s nothing inherently wrong with nested overlays, but given the fragility of PMTUD and the opacity of MPU and MRU it magnifies the risks
Let’s start at the bottom here.
We have a VXLAN overlay using UDP encapsulation on an IP underlay on an Ethernet layer-2 network
  Let’s assume an Ethernet maximum frame-size of 9214 bytes.
    To get the maximum payload size it can accommodate we’ll subtract:
      26 bytes of Ethernet headers (14 bytes required; 4 for .1q; another 4 in case some smarty-pants opts for q-in-q
      And the four-byte CRC)
    And get a 9184 byte MPU
  Now we subtract 60 bytes for IP headers
    MPU is down to 9124 bytes
  Minus another 8 bytes of UDP headers
    9116 bytes of MPU
  Minus the VXLAN header (another 8 bytes)
    9008 byte MPU
But the bottom VXLAN overlay is carrying the GENEVE overlay, which should set it’s MTU to 9008 bytes to match the MPU of the VXLAN overlay
  To get the GENEVE overlay’s MTU, we need to subtract its encapsulation overhead
    14 bytes of required Ethernet headers
    8 bytes for .1q and maybe q-in-q
      But, at least we don’t need to include the Ethernet CRC (which GENEVE and VXLAN do *not* pull in while encapsulating the inner frame
    60 bytes for IP headers
    8 bytes for UDP headers
    260 bytes for worst-case GENEVE header-length
  The GENEVE overlay’s MPU is 8658 bytes
But the GENEVE overlay is providing transport for yet another VXLAN overlay
  so we have to subtract it’s encapsulation overhead
    14 bytes of required Ethernet headers
    We’lll be generous and assume that our Kubernets cluster isn’t using .1q or qinq on its Linux vswitch for the CNI networks
    We’ll also not include the CRC, since VXLAN doesn’t encapsulate it
    60 bytes for IP headers
    8 bytes for UDP headers
    8 bytes for VXLAN headers
  Top VXLAN overlay’s MPU is down to 8568
Upwards, onwards --- to our top Ethernet layer
  It sits on top of a VXLAN overlay that has an MPU of 8568 mytes
  It has its own headers of 14 bytes (let’s assume again that the Ethernet segments in the K8s CNI aren’t bothering with .1q)
  And the 14-byte CRC trailer is ignored by the downstack VXLAN encapsulation
  So, it has an 8554 byte MPU
Which leaves us at the top of the stack, where our IP layer should have an MTU of no higher than 8554 bytes

## Slide 35: Encapsulation Ad Absurdum (pics!)
VXLAN overlay
VXLAN overlay
GENEVE overlay
IP Datagram
{Eth headers} {Payload} {CRC}
Ethernet Frame
{IP header} {Payload}
{Eth} {IP} {UDP} {VXLAN} {Payload} {CRC}
{Eth} {IP} {UDP} {GENEVE} { Payload } {CRC}
{Eth} {IP} {UDP} {VXLAN} { Payload } {CRC}
Notes: Let’s start at the bottom here.
We have a VXLAN overlay using UDP encapsulation on an IP underlay on an Ethernet layer-2 network
  Let’s assume an Ethernet maximum frame-size of 9214 bytes.
    To get the maximum payload size it can accommodate we’ll subtract:
      26 bytes of Ethernet headers (14 bytes required; 4 for .1q; another 4 in case some smarty-pants opts for q-in-q
      And the four-byte CRC)
    And get a 9184 byte MPU
  Now we subtract 60 bytes for IP headers
    MPU is down to 9124 bytes
  Minus another 8 bytes of UDP headers
    9116 bytes of MPU
  Minus the VXLAN header (another 8 bytes)
    9008 byte MPU
But the bottom VXLAN overlay is carrying the GENEVE overlay, which should set it’s MTU to 9008 bytes to match the MPU of the VXLAN overlay
  To get the GENEVE overlay’s MTU, we need to subtract its encapsulation overhead
    14 bytes of required Ethernet headers
    8 bytes for .1q and maybe q-in-q
      But, at least we don’t need to include the Ethernet CRC (which GENEVE and VXLAN do *not* pull in while encapsulating the inner frame
    60 bytes for IP headers
    8 bytes for UDP headers
    260 bytes for worst-case GENEVE header-length
  The GENEVE overlay’s MPU is 8658 bytes
But the GENEVE overlay is providing transport for yet another VXLAN overlay
  so we have to subtract it’s encapsulation overhead
    14 bytes of required Ethernet headers
    We’lll be generous and assume that our Kubernets cluster isn’t using .1q or qinq on its Linux vswitch for the CNI networks
    We’ll also not include the CRC, since VXLAN doesn’t encapsulate it
    60 bytes for IP headers
    8 bytes for UDP headers
    8 bytes for VXLAN headers
  Top VXLAN overlay’s MPU is down to 8568
Upwards, onwards --- to our top Ethernet layer
  It sits on top of a VXLAN overlay that has an MPU of 8568 mytes
  It has its own headers of 14 bytes (let’s assume again that the Ethernet segments in the K8s CNI aren’t bothering with .1q)
  And the 14-byte CRC trailer is ignored by the downstack VXLAN encapsulation
  So, it has an 8554 byte MPU
Which leaves us at the top of the stack, where our IP layer should have an MTU of no higher than 8554 bytes
So; at the very bottom of our stack, we have a maximum Ethernet frame size of 9214 bytes.
And at the very top of our stack, we have an IP interface MTU of 8554 bytes.
  That’s 660 bytes of encapsulation overhead, just within two adjacent cabinets in the same data center!
Do you trust your two different VXLAN tunnel-endpoint platforms to not break PMTUD? How ‘bout the GENEVE TEPs?
  Of course not.
So, now you have to make 8554 the maximum IP interface MTU across the entire network, to account for instances where top-layer hosts are talking to bottom-layer hosts.
If you’re running a hyper-converged compute cluster, maybe you have iSCSI running on some VLANs/subnets.
  Lucky for you, you’re still over that 8400-byte “magic number” for NFS?
  But, what if the K8s CNI was using GENEVE instead of VXLAN? That would reduce MTU by an additional 252 bytes!
    Ruh-roh!

## Slide 36: Failure to Implement PLPMTUD
PLPMTUD solves all of the problems we’ve discussed
  But, only at the packetization-layer, not at the IP Layer.
It has been part of the TCP implementation in Linux and Windows for years, but it is not enabled by default.
If your device has a TCP implementation and it’s not doing PLPMTUD?
  Shame! Shame; shame; shame.

## Slide 37: Jumbo Gumbo
It’s a (not un-)reasonable practice to set the gateway’s IP MTU to 9000 when enabling jumbo frames on an Ethernet broadcast domain.
It’s a (not un-)common practice to do this without requiring every host on the same subnet to:
  Have an L2 MRU of 9022(-ish) bytes
  Have an L3 MRU of 9000 bytes
The creates a PMTUD blackhole if any of those hosts don’t happen to have L2/L3 MRUs at least that high

## Slide 38: The List of Demands
04-Feb-2025

## Slide 39: Of Standards Bodies:
Somebody, please(!) formalize jumbo Ethernet frames already
Define the expected behavior for any message-oriented protocols when an interface receives a message larger than its interface MTU, but smaller than the protocol MTU.
Notes: I’m not saying that there has to be a single explicitly defined maximum frame size, but it would surely make things easier if there were.
And it would help avoid a lot of integration headaches if there were universally expected behavior with regards to L2 MTU and MRU.
  Like, what a jumbo-frame-capable switch is supposed to do if it receives a jumbo frame on an L2 broadcast domain without jumbo frames explicitly enabled
    Does it accept the frame, if the switch itself is the destination?
And, what is the expected behavior if an IP host receives an 8400-byte IP datagram, and its interface MTU is set to 1500-bytes? Is it required to accept and process the datagram? Is that just

## Slide 40: Of Vertical Interface Designers:
Start exposing MPU in the up-stack direction
Start consuming MPU from the down-stack direction as a basis for interface MTU inference
  If:L(n-1):MPU = If:L(n):MTU
Start exposing MTU, MRU, and MPU via the management plane
Notes: Explicitly expose MTU, MRU, and MPU in the management plane

## Slide 41: Of Makers of IP Overlay Systems:
  Your in-network-tunneling devices are both “routers” and “hosts” (please behave accordingly)
  Maintain PMTUD state on Tu interfaces for destinations on the underlays (host behavior)
  Generate PTBs when an overlay packet can’t be encapped and sent to the underlay (router behavior)
    Include the Tu interface’s path MTU when making the determination about whether MTU would be exceeded
Notes: While we’re waiting for a magical end-to-end elixir…

## Slide 42: Operators: Enforce Per-Subnet MTU
Authoritatively declare an IP MTU for every subnet that you operate
Do not permit hosts to exceed the declared MTU in their interface MTU configuration
Only permit hosts to configure interface MTU that is lower than the subnet’s declared MTU:
  If they can successfully demonstrate that their IP MRU remains at least as large as the subnet’s declared MPU
  Very begrudgingly
Include MTU option whenever DHCP is used

## Slide 43: Operators: Overlay Precautions
Always prefer the minimum required number of stacked overlays
Don’t deploy an overlay if you don’t have authoritative knowledge of the underlay’s MTU
When declaring the IP MTU for an overlay subnet, use a value less-than or equal to:
  Underlay-MTU minus Overlay-Encap-Overhead
Notes: Always prefer the minimum required number of stacked overlays
  0 overlays is best
  1 overlay is 2nd best
  2 stacked overlay is 3rd best
If you can’t be sure of the underlay MTU, you can’t be sure of the overlay MTU.
Avoid in-network IP-on-IP overlays when you can
  Provide MTU “cushion” in the underlay when you can’t avoid overlays
Enable PLPMTUD everywhere you can
Avoid encapsulation protocols with variable header-lengtss

## Slide 44: Operators: Enable PLPMTUD
Enable PLMTUD in the TCP implementation of any hosts in your networks that support it.
This solves PMTUD blackholes for TCP traffic; why are we not doing this already?

## Slide 45: Operators: Bi-modal MTU
Prefer operational models that implement a bi-modal approach to MTU.
  1500-byte MTU for the vast majority of IP-on-Ethernet subnets
  A “large-MTU” (“of best fit”) for your organization for everything using jumbo-frames and large IP packets
Notes: If you have eight different workload types that prefer to consume jumbo-frame Ethernet and use it for IP traffic, use the lowest of those 8 platforms’ “maximum MTU” as your organization’s “large MTU” value

## Slide 46: Operators: BGP Policy
Consider tagging routes when they are introduced to BGP, coding for segment MTU
And applying BGP policy to prefer paths that maximize higher end-to-end-MTU.
  This is, admittedly, much simpler if you have a bi-modal MTU approach in your organization
Notes: draft-ietf-idr-bgp-ls-link-mtu-07 proposes a new BGP-LS sub-TLV to do exactly that
  Though, only for MTUs up to 65535
In the mean-time, large community attributes are a perfectly viable alternative

## Slide 47: Well-Grounded Paths to MTU(topia?)
04-Feb-2025

## Slide 48: “MTU propagation over EVPN Overlays”
Use of ICMP multi-part extension to capture enough of the overlay-packet headers in PTBs so that tunnel interfaces can successfully translate underlay PTB into overlay PTBs
This seems very promising to me
Does put additional compute burden on TEPs, but seems relatively manageable
Notes: https://datatracker.ietf.org/doc/draft-saum-nvo3-mtu-propagation-over-evpn-overlays/
IETF Draft, expired February 1st.
I contacted the authors, and they did not have any future plans other than to renew the IETF draft
Alternate schema?
  Use IP “identifier” header to tag underlay packets and correlate them to an overlay src/dst IP addr. Pair
  When a PTB is received on an underlay interface, check the “identifier” value of the original packet to assist in xlating the PTP into overlay network
  Seems like a dead-end, since the “identifier field” seems to be headed towards “fragmented-packets-only” tasking

## Slide 49: Purely Speculative Paths to MTU(topia?)
04-Feb-2025

## Slide 50: IP/ICMP PMTUD w/ inference?
PMTUD works for all IP traffic.
  Implemented at IP/ICMP layer
PLPMTUD only requires participation by the endpoints
  Uses inference of PMTU based on correlation of packet-length and lack of acknowledgement
Can we infer PMTUD at the IP/ICMP layer?
  Yes, we can!
  We’ve all used the “ping –m do -s…” test to zero in on path MTU at some point
    Let’s bake that behavior into host’s IP interface implementations?
Notes: PMTUD is best, is because it works for all IP traffic.
  Implemented at the IP/ICMP layer
PMTUD is worst is because it requires active participation by every single hop between endpoints
  Because the detection mechanism is an explicit notification
PLPMTUD is best because it only requires participation by the endpoints
  Because the detection mechanism is an inference
    Based on strong correlation between lack-of-acknowledgement and packet size
PLPMTUD is not-the-best because it “only” protects the packetization layer (TCP, practically speaking) from PMTUD blackholes
Why can’t we use the same basic logic of PLPMTUD at the IP layer? (Infer blackholes from strong correlation between packet-size and non-ACKed packets(?)
  Because IP is stateless and has no acknowledgement mechanism
  But… ICMP has echo-request/echo-response (we’ve all used the “ping –m…” test to zero in on a path MTU
  We could bake that mechanism into an IP interface as part of PMTUD logic.
How would it work?
  Highly analogous to how PLPMTUD integrates with PMTUD.
    Would provide potential augmentation of PMTUD visibility

## Slide 51: Decouple Interface and Path MTU?
PMTUD (all varieties) are only designed to detect path MTU that is lower than the local egress interface MTU
But, as we know, interface MTU is inherently untrustworthy.
Let’s “take the leash off” of path-MTU and allow it to probe up past the local interface MTU value.
Would allow “senseless victim flows” to realize actual path MTU, even though the origin network’s MTU had been “dumbed down” because of one weak-link somewhere upstream that only some traffic was routed through.
Notes: I’m still thinking this through.
I’m pretty sure that as long as it’s only done for path-MTU values, there’s no harm.
I don’t think that TCP would be able to take advantage of this, but anything trusting the IP interface’s path-MTU could benefit

## Slide 52: Questions (and answers?)
04-Feb-2025

## Slide 53: FIN
04-Feb-2025

## Slide 55: Content Sacrificed to Time Constraints
04-Feb-2025

## Slide 56: Nested Encapsulation
Application
Presentation
Transport
IP (datagrams)
Ethernet (frames)
Notes: Now ---once again, I’m recognizing the look on a lot of the faces in the room, and that look is telling me that we’re going to just skip straight to the END of this slide….
How do we cram something that could by 65 thousand bytes long into something that can’t be more than 1522 byes long?
The original authors of the TCP/IP protocol suite were, by all accounts, “pretty smart”, so they:
Incorporated the concept of Maximum Transmission Unit (MTU) directly into the Internet Protocol
I like to think that this was only after multiple failed attempts to license “timelord TARDIS technology” from Dr. Who
Data communications network technologies are generally conceptualized using a “multi layer” model in which “upper” (or “inner”, if you prefer) layer services are hosted-on/transported-by/encapsulated on “lower” (or “outer”, if you prefer) layer services. Most of our “formal education” in the field is centered in the OSI 7-layer model, but much of our practical experience deals with the four-layer model of the Internet Protocol Suite, and the menagerie of layers introduced above (and more than occasionally) between them.
What’s the same about all those different conceptual models is that they involve taking a message, and putting it (all of it) inside a different (bigger) kind of message.
What matters about that (for the sake of this discussion) is this simple fact:
  If you want to put “thing A” inside of “thing B”, thing B must be larger than thing A.
Let’s take a quick, stroll down encapsulation boulevard:
CLICK for 1st animation
  We start with an application. It’s got something to say. Maybe it’s a video stream, maybe it’s an error message; who knows!
  This application might have a presentation layer that it interfaces with, so it sends its message to the presentation-layer to be dealt with
Click for 2nd animation
  The presentation layer does whatever it is that it needs to do, and hands the application’s message (now embedded in the payload of a presentation-layer message) to a transport-layer interface
Click for 3rd animation
  Maybe it’s TCP, maybe it’s UDP, I don’t even care --- I’m just trying to make a point here!
  That transport layer (and let’s be honest, you know it was TCP or UDP.) is going to hand it off too…
Click for 4th animation
  Now, let’s be real. IP over Ethernet is approximately 110% of the typical enterprises network footprint. And IP MTU is what I’m here to talk to you about today
  So, a bit more detail about the IP layer…
    It’s a “message-oriented” protocol, not a “streaming” protocol.
      Every “message” has a discrete beginning and a discrete end.
      Messages aren’t valid unless they are complete.
      These messages are most precisely referred to as “datagrams” (but are ubiquitously referred to as “packets.”)
      IPv4 has a built-in maximum message/datagram/packet size of 65535 bytes.
Click for 5th animation.
  Ethernet! Ethernet is like oxygen for enterprise networks, so we’ll focus on Ethernet as the bottom/outer-most encapsulating protocol in this talk
  There are many “flavors” of Ethernet; we’ll discuss 802.3 initially.
  Ethernet, like IP, is a message-oriented protocol
  We call these messages “frames” (many people call them “packets”, usually in the context of a discussion where the difference between Ethernet frames and IP packets is the crux of the issue.)
  An 802.3 Ethernet frame as a maximum frame-size of 1520 bytes.
So, there it is. That’s “the problem”.
  How do we cram something that could by 65 thousand bytes long into something that can’t be more than 1522 byes long?
    The original authors of the TCP/IP protocol suite were, by all accounts, “pretty smart”, so they:
      Incorporated the concept of Maximum Transmission Unit (MTU) directly into the Internet Protocol
      I like to think that this was only after multiple failed attempts to license “timelord TARDIS technology” from Dr. Who
Graphic attribution: https://www.goodfon.com/space/wallpaper-shar-matrioshka-kosmos-zemlia-zemlia.html
Graphic license: https://creativecommons.org/licenses/by-nc/4.0/

## Slide 57: IP / Ethernet
IP and Ethernet are both message oriented protocols
  Nothing in a message is valid until you’re sure that the message has ended
IP and Ethernet both have innate limits on the size of message that they can transmit
  IP datagram maximum size: 65535 bytes
  Ethernet frame maximum size: (roughly) 11455 bytes
Notes: IP and Ethernet are “message-oriented” protocols, as opposed to streaming protocols. Data is transported in discrete chunks (“messages”).
  The “messages” of IP are referred to as “datagrams” (less precisely referred to as “packets” by 99% of us approximately 102% of the time.)
  The “messages of Ethernet are referred to as “frames”
Another thing that both IP and Ethernet protocols have in common is a maximum permitted size for their messages
  IP has a maximum datagram (aka packet) size of 65535 bytes
  Ethernet (the 802.3 flavor) has a maximum frame size of 1520 bytes
Let’s look at how we establish the maximum viable IP MTU for an interface transmitting an 802.3 Ethernet frames
We’ll start with our old friend the Ethernet frame.
CLICK for animation 1.
The Ethernet frame format has defined sections that we care about here:
  Headers: Taking up 18 bytes (I’m oversimplifying here, but bear with me)
    CLICK for animation 2
  The Payload: Taking up as much as 1500 bytes
    CLICK for animation 3
  The CRC: Taking up 4 bytes
    CLICK for animation 4
Ahh yes, The payload section, we’ll get back to THAT momentarily. But first…
But setting the Ethernet frame aside momentarily, here comes our best pal, the IP datagram
  CLICK for animation 5
An IP datagram will *always* start with some headers (20-6-bytes)
  CLICK for animation 6
And after the headers, there’s room for the payload.
  CLICK for animation 7
Now, of course, IP and Ethernet are like Peanut-butter and jelly, so of COURSE, they end up together.
  CLICK for animation 8
So, where are we at?
  If “vanilla” 802.3 Ethernet is at the bottom of our stack; we know that it has a 1500-byte maximum payload
  The “payload” section of the Ethernet frame is what will contain the IP datagram (byte for byte; the whole shebang.)
  When RFC 791 defines the IP MTU as ““the maximum sized datagram that can be transmitted through the next network”, it could also have said:
    The maximum size of the payload field of the next-layer encapsulating protocol.
  So, we know that our Ethernet network can handle frames that are up to 1522 bytes long, but only 1500 of those bytes are available to “hold” our IP datagrams.
    That’s where we get “1500” as the standard MTU value for IP interfaces that are bound to 802.3 Ethernet interfaces
This diagram depicts the encapsulation of an IP datagram in an 802.3 Ethernet frame
The following diagram visually depicts the relationship of IP and Ethernet to each other, with an IP protocol packet being “encapsulated” into a surrounding Ethernet frame. It’s important to note that both protocols/formats have their own “payload” and “header” sections, which contribute to their overall length. The “payload” is the data that each protocol accepts from the immediately-upper-layer service. The “header” is the protocol’s own data.
IP packet/datagram. Protocol-maximum size: 65535 bytes
IP transit interface’s configured MTU must not be greater than the maximum payload size of the associated Layer-2 interface

## Slide 58: IP / Ethernet Encapsulation
IP datagram
Headers (20-60 bytes)
Payload (0-1440 bytes)
Ethernet Frame
Headers (18 bytes)
Payload (46-1500 bytes)
CRC (4 bytes)
Notes: Let’s look at how we establish the maximum viable IP MTU for an interface transmitting an 802.3 Ethernet frames
We’ll start with our old friend the Ethernet frame.
CLICK for animation 1.
The Ethernet frame format has defined sections that we care about here:
  Headers: Taking up 18 bytes (I’m oversimplifying here, but bear with me)
    CLICK for animation 2
  The Payload: Taking up as much as 1500 bytes
    CLICK for animation 3
  The CRC: Taking up 4 bytes
    CLICK for animation 4
Ahh yes, The payload section, we’ll get back to THAT momentarily. But first…
But setting the Ethernet frame aside momentarily, here comes our best pal, the IP datagram
  CLICK for animation 5
An IP datagram will *always* start with some headers (20-6-bytes)
  CLICK for animation 6
And after the headers, there’s room for the payload.
  CLICK for animation 7
Now, of course, IP and Ethernet are like Peanut-butter and jelly, so of COURSE, they end up together.
  CLICK for animation 8
So, where are we at?
  If “vanilla” 802.3 Ethernet is at the bottom of our stack; we know that it has a 1500-byte maximum payload
  The “payload” section of the Ethernet frame is what will contain the IP datagram (byte for byte; the whole shebang.)
  When RFC 791 defines the IP MTU as ““the maximum sized datagram that can be transmitted through the next network”, it could also have said:
    The maximum size of the payload field of the next-layer encapsulating protocol.
  So, we know that our Ethernet network can handle frames that are up to 1522 bytes long, but only 1500 of those bytes are available to “hold” our IP datagrams.
    That’s where we get “1500” as the standard MTU value for IP interfaces that are bound to 802.3 Ethernet interfaces
This diagram depicts the encapsulation of an IP datagram in an 802.3 Ethernet frame
The following diagram visually depicts the relationship of IP and Ethernet to each other, with an IP protocol packet being “encapsulated” into a surrounding Ethernet frame. It’s important to note that both protocols/formats have their own “payload” and “header” sections, which contribute to their overall length. The “payload” is the data that each protocol accepts from the immediately-upper-layer service. The “header” is the protocol’s own data.
IP packet/datagram. Protocol-maximum size: 65535 bytes
IP transit interface’s configured MTU must not be greater than the maximum payload size of the associated Layer-2 interface

## Slide 59: Ethernet Jumbo Frames
What are they?
  Ethernet frames without the 1500-byte payload limit.
  No standards defined
Notes: What are jumbo frames?
  We could spend 30 days discussing that question and not reach a satisfying answer.
  The “Ethernet Alliance” published a position paper in November of 2009 that summarized things pretty well.
    https://www.ethernetalliance.org/wp-content/uploads/2011/10/EA-Ethernet-Jumbo-Frames-v0-1.pdf
  Long-story short: They’re Ethernet frames, without the 1500-byte payload limit.
How do they work?
  There’s no “length” field in the headers to worry about (the Ethertype field is interpreted as length only for values <=1500.
  There *is* the cyclic-redundancy-check (CRC) at the end of frame that we need to worry about.
    The last four bytes of an Ethernet frame are defined as a CRC.
      Since an Ethernet frame doesn’t have a fixed length, that means we have to wait for the interframe-gap to be sure we’ve seen the end of the frame.
      Ethernet uses the CRC-32 algorithm, which…
        Is a one-way hash function.
        And has roughly equivalent probability for undetected errors for frame-sizes ranging from 376 to 11,455 bytes
          With the undetected error probability increasing above 11,455 bytes
          http://staff.psc.edu/mathis/MTU/AlteonExtendedFrames_W0601.pdf
            According to an Alteon Whitepaper from 2011
              Presumably some combination of:
                Exponentially more possible messages means a greater probability of two messages having the same hash value
                As frame sizes increase the probability of multiple bit errors also increases
    Ethernet’s CRC-32 algorithm provided similar probabilities for missed-errors at frame sizes of up, 11,455 bytes.
      Extended Frame Sizes for Next Generation Ethernets @ https://web.archive.org/web/20110807131142/staff.psc.edu/mathis/MTU/AlteonExtendedFrames_W0601.pdf
        Published by Alteon Networks
    So… “how they work” is “you adjust your maximum frame-size up from 1522(-ish) bytes to a bigger number.

## Slide 60: Ethernet Jumbo Frames (3)
Advantages | Disadvantages
Increased throughput | Increased latency
Decreased CPU utilization | Increased queue requirements
Key enabler for IP-storage | Need end-to-end enablement
Fix so many problems | Cause so many problems
Notes: Advantages of Jumbo Frames
  Larger MTUs have a positive correlation with increased TCP throughput (under certain conditions)
    Table of Maximum TCP throughput for various latency
  MTU sizes are inversely correlated with CPU utilization on sending/receiving hosts
    A larger MTU means more data to be transported in fewer packets (per total payload data).
    Fewer packets means less CPU cycles spent parsing packet headers (per total payload data).
      Calculating Ethernet and TCP CRC values
      Validating MAC and IP addressing
      Etc.…
Dis-advantages of Jumbo Frames
  Increased latency
  Inefficiencies on switching platforms queueing mechanisms
  Upper-lay protocol stack inefficiencies (after years and years of optimization for 1500-byte Ethernet max. payloads)
  Requires a discovery mechanism to take full advantage

## Slide 61: IP / Jumbo-Ethernet Encapsulation
IP datagram
Headers (20-60 bytes)
Payload (0- bytes)
Ethernet Frame
Headers (18 bytes)
Payload (46- bytes)
CRC (4 bytes)
8940
8940
Notes: Well, this looks a lot like the figure from two slides ago.
The only difference is that 6x increase in the maximum size of the Ethernet payload
  And, therefore the IP MTU

## Slide 62: PMTUD: Why?
The lowest interface MTU on the entire path between two IP endpoints is the path MTU (aka “effective MUT”).
We want an IP interface to be able to discover and maintain path-MTU information for cases when the path-MTU is lower than the interface MTU.
Notes: Path MTU Discovery (PMTUD)
  Defined in RFC1191/RFC1981 (Internet Standard)
  Uses the don’t-fragment option in IP datagrams in conjunction with ICMP “fragmentation needed and DF set" messages from transit nodes between two endpoints to discover the “effective MTU” between two endpoints.
  Implemented at the IP-layer
Packetization-layer PMTUD (PLPMTUD)
  Defined in RFC4821
  Does *not* rely on ICMP PTB messages from transit nodes
  Implemented “above” the IP-layer in a packetization protocol
    Such as TCP
      But *not* UDP, which is a datagram protocol, not a packetization protocol
  In Windows as part of the TCP implementation (a shadow registry key that has to be explicitly added)
    HKEY_LOCAL_MACHINE\SYSTEM\CurrentControlSet\Services\Tcpip \Parameters\EnablePMTUBHDetect
  In Linux (disabled by default)
    /proc/sys/net/ipv4/tcp_mtu_probing
      (circa 2007?)
Datagram Packetization Layer Path MTU Discovery (DPLPMTUD)
  Defined in RFC 8899 (Proposed Internet Standard, 2020)
  Baked into Linux’s SCTP implementation as of roughly 2021(?)
Path MTU Discovery (PMTUD) should be sufficient to allow for a network with an arbitrary MTU (1500 bytes) to operate in an environment where an upstream transport network operates with a smaller MTU (e.g.., 1460 bytes) - If hosts A and B on network-A send 1500-byte IP packets to each other, they will be dropped by the upstream transit network, and ICMP PTB messages we be sent back to the sender,indicating a path-MTU of 1460 bytes should be assumed for the existing socket - There are plenty of real-world obstacles to PMTUD operation - ICMP blackholes (firewall rules, ECMP routing decisions sending the ICMP PTB messages to a different host than the one that sent the over-sized packet) - Same-subnet MTU mismatches

## Slide 63: PMTUD: RFC1191
Oldest, most abundant PMTUD mechanism
Operates exclusively in the IP and ICMP layers
Requires every IP gateway in the path to do its part
Results in explicit/correct PMTU value
Notes: Path MTU Discovery (PMTUD)
  Defined in RFC1191/RFC1981 (Internet Standard)
  Uses the don’t-fragment option in IP datagrams in conjunction with ICMP “fragmentation needed and DF set" messages from transit nodes between two endpoints to discover the “effective MTU” between two endpoints.
  Implemented at the IP-layer
Packetization-layer PMTUD (PLPMTUD)
  Defined in RFC4821
  Does *not* rely on ICMP PTB messages from transit nodes
  Implemented “above” the IP-layer in a packetization protocol
    Such as TCP
      But *not* UDP, which is a datagram protocol, not a packetization protocol
  In Windows as part of the TCP implementation (a shadow registry key that has to be explicitly added)
    HKEY_LOCAL_MACHINE\SYSTEM\CurrentControlSet\Services\Tcpip \Parameters\EnablePMTUBHDetect
  In Linux (disabled by default)
    /proc/sys/net/ipv4/tcp_mtu_probing
      (circa 2007?)
Datagram Packetization Layer Path MTU Discovery (DPLPMTUD)
  Defined in RFC 8899 (Proposed Internet Standard, 2020)
  Baked into Linux’s SCTP implementation as of roughly 2021(?)
Path MTU Discovery (PMTUD) should be sufficient to allow for a network with an arbitrary MTU (1500 bytes) to operate in an environment where an upstream transport network operates with a smaller MTU (e.g.., 1460 bytes) - If hosts A and B on network-A send 1500-byte IP packets to each other, they will be dropped by the upstream transit network, and ICMP PTB messages we be sent back to the sender,indicating a path-MTU of 1460 bytes should be assumed for the existing socket - There are plenty of real-world obstacles to PMTUD operation - ICMP blackholes (firewall rules, ECMP routing decisions sending the ICMP PTB messages to a different host than the one that sent the over-sized packet) - Same-subnet MTU mismatches

## Slide 64: PMTUD: RFC4821 / PLPMTUD
Executed exclusively on the endpoints
Operates at the packetization layer (e.g.. TCP)
Infers path MTU based on the size of packets sent but not ACKed
Implies the need for a path information cache at the IP layer

## Slide 65: PMTUD: RFC8899 / DPLPMTUD
Defines a pattern for applications using datagram transport protocols (e.g. UDP) implement PLPMTUD.
Has to be implemented in the application

## Slide 66: PMTUD: Recap
 | Layer of Operation | Must run on? | Notes
RFC1191 | IP/ICMP | All senders and all gateways | Best juice:squeeze ratio on endpoints.
RFC4821 | Packetization (e.g.. TCP) | Endpoints only, but all packetization-layer Ifs | Basically solves PMTUD for all TCP
RFC8899 | Application (e.g.. SCTP) | Endpoints only, but all applications. | Per-application implementation is a big ask

## Slide 67: Ethernet Jumbo Frames
Ethernet uses CRC32 for error-detection
  Probability of missed-errors increases sharply above 11,455-byte frame-length
8400 bytes of payload was regarded as a bit of a magic number
Ethernet headers keep getting bigger
Notes: Why ~9,000 bytes?
  The CRC-32 algorithm used in the Ethernet FCS imposes a practical limitation of maximum Ethernet frame-size of 11,455 bytes.
  The same Alteon whitepaper from 13 years ago also points out that an NFS datagram is 8400-bytes, and
    After accounting for the additional overhead of Ethernet, IP, UDP, RPC, and XDR encapsulation, that 8400-byte NFS datagram fits quite nicely into a 8443-byte Ethernet frame.
    How did we get from 8443 to ~9000 though?
      The thinking seems to have been “let’s try to stick to multiples of the original maximum frame-length for the new “jumbo frame” maximum frame size.
        Sort of, it’s actually multiple of the maximum *payload* length of 1500 bytes.
          6*1500 =9000
          5*1500=7500
Love ‘em or hate ‘em – they’re *here*, and we’d better get used to it.